R34 - 1,000 km (600 Miles) Service

Engine and Emission Control Maintenance

Inspect and correct or replace as necessary:

- engine oil level

- engine coolant level

- brake fluid level

- windshield washer fluid level

- battery fluid level

- idle RPM

- drive belts.

# Chassis and Body Maintenance

Inspect and correct or replace as necessary:

- steering gear and linkage

- axle

- suspension parts

- prop shaft

- drive shafts

Information derived from R34 Nissan Skyline Owners Manual (Nissan Japan) and R34 Nissan Skyline Vehicle Warranty and Owners Identification Manual (Nissan New Zealand)

R34 - 10,000 km (6,000 Miles)/6 Months Service

Engine and Emission Control Maintenance

Replace:

- engine oil

- engine oil filter.

Chassis and Body Maintenance

Inspect and correct or replace as necessary:

- brake, clutch and auto transmission fluid levels and for leakage

- power steering fluid levels and lines for leakage

- braking systems

- clutch system

- exhaust system

- manual transmission, front and rear differentials and transfer case oils for levels and leakage

- brake pads, discs and associated brake components

- foot brake, park brake and clutch for free play, stroke and operation.

Lubricate:

- locks, hinges and bonnet/boot latches.

R34 - 20,000 km (12,000 Miles)/12 Months Service

Engine and Emission Control Maintenance

Replace:

- engine oil

- engine oil filter.

Inspect and correct or replace as necessary:

- valve clearances if there is an increase in valve noise

- engine cooling system.

# Chassis and Body Maintenance

Replace:

- ventilation air filter.

Inspect and correct or replace as necessary:

- brake, clutch and auto transmission fluid levels and for leakage

- power steering fluid levels and lines for leakage

- braking systems

- clutch system

- exhaust system

- manual transmission, front and rear differentials and transfer case oils for levels and leakage

- steering gear and linkage

- axle

- suspension parts

- prop shaft

- drive shafts

- wheel alignment, rotation and balance of wheels

- brake pads, discs and associated brake components

- foot brake, park brake and clutch for free play, stroke and operation.

- seat belt, buckles, retractors, anchors and adjuster

Lubricate:

- locks, hinges and bonnet/boot latches.

R34 - 30,000 km (18,000 Miles)/18 Months Service

Engine and Emission Control Maintenance

Replace:

- engine oil

- engine oil filter.

Chassis and Body Maintenance

Inspect and correct or replace as necessary:

- brake, clutch and auto transmission fluid levels and for leakage

- power steering fluid levels and lines for leakage

- braking systems

- clutch system

- exhaust system

- manual transmission, front and rear differentials and transfer case oils for levels and leakage

- brake pads, discs and associated brake components

- foot brake, park brake and clutch for free play, stroke and operation.

Lubricate:

- locks, hinges and bonnet/boot latches.

R34 - 40,000 km (24,000 Miles)/24 Months Service

Engine and Emission Control Maintenance

Replace:

- engine oil

- engine oil filter.

Inspect and correct or replace as necessary:

- valve clearances if there is an increase in valve noise

- drive belts

- engine coolant mixture ratio

- cooling system

- fuel lines

- EVAP vapour lines

- heated oxygen sensor.

Chassis and Body Maintenance

Replace:

- brake fluid

- front and rear differentials and transfer case oils

- ventilation air filter.

Inspect and correct or replace as necessary:

- brake, clutch and auto transmission fluid levels and for leakage

- brake booster vacuum hoses, connections and check valve

- power steering fluid levels and lines for leakage

- braking systems

- clutch system

- exhaust system

- manual transmission gear oil for levels and leakage

- steering gear and linkage

- axle

- suspension parts

- prop shaft

- drive shafts

- wheel alignment, rotation and balance of wheels

- brake pads, discs and associated brake components

- foot brake, park brake and clutch for free play, stroke and operation.

- seat belt, buckles, retractors, anchors and adjuster

Lubricate:

- locks, hinges and bonnet/boot latches.

R34 - 50,000 km (30,000 Miles)/30 Months Service

Engine and Emission Control Maintenance

Replace:

- engine oil

- engine oil filter

- air cleaner filter (viscous type)

- fuel filter.

Chassis and Body Maintenance

Inspect and correct or replace as necessary:

- brake, clutch and auto transmission fluid levels and for leakage

- power steering fluid levels and lines for leakage

- braking systems

- clutch system

- exhaust system

- manual transmission, front and rear differentials and transfer case oils for levels and leakage

- brake pads, discs and associated brake components

- foot brake, park brake and clutch for free play, stroke and operation.

Lubricate:

- locks, hinges and bonnet/boot latches.

R34 - 60,000 km (36,000 Miles)/36 Months Service

Engine and Emission Control Maintenance

Replace:

- engine oil

- engine oil filter.

Inspect and correct or replace as necessary:

- valve clearances if there is an increase in valve noise

- engine cooling system.

Chassis and Body Maintenance

Replace:

- ventilation air filter.

Inspect and correct or replace as necessary:

- brake, clutch and auto transmission fluid levels and for leakage

- power steering fluid levels and lines for leakage

- braking systems

- clutch system

- exhaust system

- manual transmission, front and rear differentials and transfer case oils for levels and leakage

- steering gear and linkage

- axle

- suspension parts

- prop shaft

- drive shafts

- wheel alignment, rotation and balance of wheels

- brake pads, discs and associated brake components

- foot brake, park brake and clutch for free play, stroke and operation.

- seat belt, buckles, retractors, anchors and adjuster

Lubricate:

- locks, hinges and bonnet/boot latches.

R34 - 70,000 km (42,000 Miles)/42 Months Service

Engine and Emission Control Maintenance

Replace:

- engine oil

- engine oil filter.

Chassis and Body Maintenance

Inspect and correct or replace as necessary:

- brake, clutch and auto transmission fluid levels and for leakage

- power steering fluid levels and lines for leakage

- braking systems

- clutch system

- exhaust system

- manual transmission, front and rear differentials and transfer case oils for levels and leakage

- brake pads, discs and associated brake components

- foot brake, park brake and clutch for free play, stroke and operation.

Lubricate:

- locks, hinges and bonnet/boot latches.

R34 - 80,000 km (48,000 Miles)/48 Months Service

Engine and Emission Control Maintenance

Replace:

- engine oil

- engine oil filter

- engine coolant.

Inspect and correct or replace as necessary:

- valve clearances if there is an increase in valve noise

- drive belts

- cooling system

- fuel lines

- EVAP vapour lines

- heated oxygen sensor.

Chassis and Body Maintenance

Replace:

- brake fluid

- front and rear differentials and transfer case oils

- ventilation air filter.

Inspect and correct or replace as necessary:

- brake, clutch and auto transmission fluid levels and for leakage

- brake booster vacuum hoses, connections and check valve

- power steering fluid levels and lines for leakage

- braking systems

- clutch system

- exhaust system

- manual transmission gear oil for levels and leakage

- steering gear and linkage

- axle

- suspension parts

- prop shaft

- drive shafts

- wheel alignment, rotation and balance of wheels

- brake pads, discs and associated brake components

- foot brake, park brake and clutch for free play, stroke and operation.

- seat belt, buckles, retractors, anchors and adjuster

Lubricate:

- locks, hinges and bonnet/boot latches.

R34 - 90,000 km (54,000 Miles)/54 Months Service

Engine and Emission Control Maintenance

Replace:

- engine oil

- engine oil filter.

Chassis and Body Maintenance

Inspect and correct or replace as necessary:

- brake, clutch and auto transmission fluid levels and for leakage

- power steering fluid levels and lines for leakage

- braking systems

- clutch system

- exhaust system

- manual transmission, front and rear differentials and transfer case oils for levels and leakage

- brake pads, discs and associated brake components

- foot brake, park brake and clutch for free play, stroke and operation.

Lubricate:

- locks, hinges and bonnet/boot latches.

R34 - 100,000 km (60,000 Miles)/60 Months Service

Engine and Emission Control Maintenance

Replace:

- engine oil

- engine oil filter

- air cleaner filter (viscous type)

- fuel filter

- spark plugs (platinum type)

- timing belt.

Inspect and correct or replace as necessary:

- valve clearances if there is an increase in valve noise

- engine cooling system.

Chassis and Body Maintenance

Replace:

- ventilation air filter

- manual transmission oil.

Inspect and correct or replace as necessary:

- brake, clutch and auto transmission fluid levels and for leakage

- power steering fluid levels and lines for leakage

- braking systems

- clutch system

- exhaust system

- manual transmission, front and rear differentials and transfer case oils for levels and leakage

- steering gear and linkage

- axle

- suspension parts

- prop shaft

- drive shafts

- wheel alignment, rotation and balance of wheels

- brake pads, discs and associated brake components

- foot brake, park brake and clutch for free play, stroke and operation.

- seat belt, buckles, retractors, anchors and adjuster

Lubricate:

- locks, hinges and bonnet/boot latches.

R34 Severe Conditions

The maintenance schedules listed here do not take into account driving under severe conditions. Nissan considers the following conditions as severe:

- driving under dusty conditions

- driving repeatedly short distances

- towing a trailer or caravan

- extensive idling

- driving in extremely adverse weather conditions or in areas where ambient temperatures are either extremely low or extremely high

- driving in high humidity areas or in mountainous areas

- driving in areas using salt or other corrosive materials

- driving on rough and/or muddy roads or in the desert

- driving with frequent use of braking or in mountainous areas

Driving under dusty conditions

- replace engine oil more frequently

- replace oil filter every 5,000 km (3,000 Miles)

- replace air cleaner filter every 20,000 km (12,000 Miles) or 12 months

- replace fuel filter every 20,000 km (12,000 Miles) or 12 months

- check brake pads, discs and brake components every 5,000 km (3,000 Miles) or 3 months

- replace ventilation air filter more frequently

Driving repeatedly short distances

- replace engine oil more frequently

- replace oil filter every 5,000 km (3,000 Miles)

Towing a trailer or caravan

- replace engine oil more frequently

- replace oil filter every 5,000 km (3,000 Miles)

- replace automatic transmission oil every 40,000 km (24,000 Miles) or 24 months

- replace limited slip differential gear oil every 20,000 km (12,000 Miles) or 12 months

- check brake pads, discs and brake components every 5,000 km (3,000 Miles) or 3 months

- check propeller and drive shafts every 10,000 km (6,000 Miles) or 6 months

Extensive idling

- replace engine oil more frequently

- replace oil filter every 5,000 km (3,000 Miles)

Driving in extremely adverse weather conditions or in areas where ambient temperatures are either extremely low or extremely high

- replace fuel filter every 20,000 km (12,000 Miles) or 12 months

Driving in high humidity areas or in mountainous areas

- replace brake fluid every 20,000 km (12,000 Miles) or 12 months

Driving in areas using salt or other corrosive materials

- check brake pads, discs and brake components every 5,000 km (3,000 Miles) or 3 months

- check steering gear and linkage, axle and suspension parts, and exhaust system every 10,000 km (6,000 Miles) or 6 months

- lubricate locks, hinges and bonnet/boot latches every 5,000 km (3,000 Miles) or 3 months

Driving on rough and/or muddy roads or in the desert

- check steering gear and linkage, axle and suspension parts, and exhaust system every 10,000 km (6,000 Miles) or 6 months

- replace automatic transmission oil every 40,000 km (24,000 Miles) or 24 months

- replace limited slip differential gear oil every 40,000 km (24,000 Miles) or 24 months

- check brake pads, discs and brake components every 5,000 km (3,000 Miles) or 3 months

- check propeller and drive shafts every 10,000 km (6,000 Miles) or 6 months

Driving with frequent use of braking or in mountainous areas

- check brake pads, discs and brake components every 5,000 km (3,000 Miles) or 3 months